## Slide 1
NAME: Goh Su Yuin STUDENT ID: 33521301 PROJECT NAME: Valorization of Palm Kernel Shell-Derived Bio-Oil via One-Pot Esterification and Azeotropic Distillation for Marine Fuel Blending
FYP A Interview (Week 8)

## Slide 2
INTRODUCTION
References:
[1] https://www.engine.online/news/eu-maritime-emissions-rose-in-2025-as-more-ships-entered-mrv-reporting-scope-7e85
[2] https://maritime-professionals.com/understanding-the-2023-imo-hgh-strategy/
[3] https://safety4sea.com/icct-global-ghg-emissions-from-shipping-2016-2023/
Maritime industry heavily dependent on fossil fuels
Total greenhouse gas emissions rose by 2.1% in 2025 [1]
Figure 2: International Maritime Organization (IMO) GHG Strategy targets [2]
Figure 1: CO2 emissions by maritime class [3]

## Slide 3
References:
[1] https://mr-marinegroup.com/methanol-fuel-advantages-and-disadvantages/
[2] https://www.wartsila.com/insights/article/ammonia-fuel-for-thought-in-our-deep-dive
EXISTING STRATEGIES
The two common efforts on decreasing maritime GHG emissions:
Methanol
Lower energy density [1].
High production cost [1].
Requires specific engine modifications and lubricants [1].
Toxicity and safety concerns [1].
Ammonia
Lower energy density [2].
Toxic and corrosive [2].
Produces harmful exhaust pollutants (Nitrogen Oxides) [2].
Increase health and safety concern [2].
No single fuel solves the problem across all shipping segments

## Slide 4
PROPOSED METHOD
References:
[1] https://pubs.acs.org/acsodf/article/8/47/44586/341370/Upgrading-Pyrolysis-Bio-Oil-through-Esterification
[3] https://marineinspection.app/blog/alternative-marine-fuels-lng-methanol-ammonia-hydrogen-shipping
[4] https://jopr.mpob.gov.my/pilot-scale-biochar-production-from-palm-kernel-shell-pks-in-a-fixed-bed-allothermal-reactor/
Pyrolysis converts biomass waste into:
  Syngas
  Pyrolysis bio-oil (PBO)
  Biochar
Crude PBO characteristics [1]:
  High acidity
  High water content
Palm kernal shell (PKS)-derived PBO chosen as feedstock due to its abundant biomass availability in Malaysia [4]
https://pyrotechenergy.com/syngas/
https://link.springer.com/article/10.1007/s42773-024-00350-1/figures/6
Bio-oil blending:
Lowest-friction route to regulatory compliance [3].
No major engine modification needed [3].
ISO 8217:2024 allows blends up to 100% blend [3].

## Slide 5
References:
[1] https://www.sciencedirect.com/science/article/pii/S0378382016301047
[2] https://www.sciencedirect.com/science/article/pii/S2772443322000186
[3] https://pmc.ncbi.nlm.nih.gov/articles/PMC13502472/
LITERATURE REVIEW
Hydrotreatment [1] | Catalytic Cracking [2] | Esterification [3]
Reacts bio-oil with H₂ gas over a catalyst to remove oxygen, forming a stable hydrocarbon fuel. Limitations: high pressure/temperature, H₂ supply, expensive catalysts. | Uses solid acid catalysts at high temperature to break large oxygenated acids into smaller hydrocarbons. Limitations: high temperature; risk of coke formation on catalyst. | A simpler, cheaper route converting carboxylic acids into less corrosive esters using alcohol. Limitations: forms excess water as a byproduct, which inhibits the reaction and limits conversion.
Esterification: Acid + Alcohol ⇌ Ester + Water
Bio-oil upgrading methods:

## Slide 6
References:
[1] https://www.jalonzeolite.com/how-do-molecular-sieves-work/
[2] https://www.sciencedirect.com/science/article/pii/S209580992500606X
[3] https://www.sciencedirect.com/science/article/pii/S1387181121000111
[4] https://pmc.ncbi.nlm.nih.gov/articles/PMC13502472/
LITERATURE REVIEW
Water removal:
Molecular Sieves / Adsorbents [1,2] | Membrane Pervaporation [3]
Solid materials (e.g., silica gel) selectively remove water molecules based on their tiny pore sizes and high polar affinity. Limitations: prone to clogging and fouling, sorbent needs heated/dried regeneration before reuse. | Hydrophilic membrane + vacuum selectively removes water; effective for continuous processes. Limitations: expensive, prone to fouling.
Azeotropic Distillation [4]
Entrainer breaks the azeotrope of alcohol- water, allowing continuous distillation and recovery of alcohol. Well suited to continuous, one-pot operation.

## Slide 7
References:
[5] https://www.mdpi.com/1996-1073/5/8/2683
[6] https://pmc.ncbi.nlm.nih.gov/articles/PMC12347235/
[7] https://pubs.acs.org/iecred/article/50/3/1171/1219556/Kinetics-of-Catalytic-Esterification-of-Propionic
LITERATURE REVIEW
Alcohol
Option | Key Consideration
1-Hexanol [1] | High BP (157°C) compared to water; act as entrainer Expensive, limited large-scale renewable production
Methanol [2,3] | Widely used in studies due to high reactivity and low BP (64.7°C); reduces energy consumption Rapid vapour generation, poor temperature control
Ethanol [3,4] | High BP (78.4°C) as compared to methanol, favourable for retention during azeotropic distillation Renewable and economical
Catalyst
Option | Key Consideration
H₂SO₄ (liquid) | Highly active, widely used in industry [5] Causes corrosion and is hard to separate from bio-oil [6]
Amberlyst-15 (Sulfonic acid based; Solid) | Reusable, easily separated Lower acid-site density (≥4.7 eq/kg) → slower rate expected [7]
Amberlyst-36 (Sulfonic acid based; Solid) | Reusable, easily separated Higher acid-site density (≥5.40 eq/kg) → faster rate expected [7]

## Slide 8
References:
[8] https://www.homepages.ed.ac.uk/jwp/Chemeng/azeotrope/hetero.html
LITERATURE REVIEW
Type | Azeotropic BP with H₂O [8] | Key Consideration
Benzene | ~69.3°C | Traditional academic reference Lowest azeotropic temperature Highly carcinogenic — serious health & safety concerns
Ethyl acetate | ~70.4°C | Considered as greener, less-toxic polar solvent Partially miscible with water → poor phase separation, contaminates distilled water
n-Heptane | ~79.2°C | Widely used non-polar entrainer Higher azeotropic temperature → greater risk of thermal degradation, polymerisation, catalyst deactivation
Cyclohexane | ~69.8°C | Second-lowest azeotropic temperature Immiscible with water → clean phase separation with minimal thermal stress
Entrainer

## Slide 9
References:
[9] https://onlinelibrary.wiley.com/doi/10.1155/2017/8359238
[10] https://doi.org/10.1007/s10553-025-01876-1
[11] https://doi.org/10.1021/ef8009266
[12] https://doi.org/10.1021/acs.energyfuels.5c06144
PROBLEM STATEMENT
Existing bio-oil esterification studies each miss part of the solution:
PKS bio-oil: reported with H₂SO₄ (corrosive catalyst) and molecular sieves (batch water removal) [9]
No entrainer: water accumulates and reverse hydrolysis limits conversion [10]
With entrainer: reported on hardwood, wood and waste oils [11, 12]
No study has combined a solid acid catalyst, ethanol and an entrainer to upgrade PKS-derived bio-oil.
RESEARCH GAP/ NOVELTY
Feedstock: PKS-derived PBO
Catalyst and alcohol: Amberlyst-36 and ethanol
Process: One-pot Dean–Stark with cyclohexane to remove water continuously at ~70°C (lower thermal stress)

## Slide 10
References:
AIM & OBJECTIVE
To develop a one-pot azeotropic esterification process for PKS-derived PBO to simultaneously reduce acid value and water content, enhancing its suitability as a low-carbon MFO component.
To investigate the effectiveness of ethanol and Amberlyst-36 in reducing acidity through esterification process
To evaluate the efficiency of cyclohexane (entrainer) in removing the water continuously generated during esterification
To optimize the key operating parameters for reducing acid value and water content of bio-oil
To characterize and compare the physio-chemical properties of crude and upgraded bio-oil after optimization

## Slide 11
References: Lindfors, T. Ohra-aho, and A. Oasmaa, “Quality Improvement of Biomass Pyrolysis Oil through Esterification,” Energy & Fuels, vol. 40, no. 33, pp. 18262–18273, Aug. 2026, doi: 10.1021/acs.energyfuels.6c01498.
PROCEDURE
Figure 5: One-pot Esterification and Azeotropic distillation from
Analytical Methods
Acid value: Acid-base titration
Water content: Karl-Fischer
Range of operating conditions:
Temperature: 70°C
Catalyst dose: 0-2 wt%
Alcohol dose: 0-60wt%
Time: 1-24 hour
Pressure: 200-1013 mbar

## Slide 12
References:
GANTT CHART

## Slide 13
References:
Ilin, A. V., Burov, N. O., Rutskoy, M. D., Savelenko, V. D., Aleksanyan, D. R., Makhova, U. A., Vikhritskaya, A. O., Klimov, N. A., Lobashova, M. M., Kapustin, V. M., & Ershov, M. A. (2025). Enhanced Upgrading of Bio-Oil for Efficient Co-Processing in Refinery Delayed Coking Units. Chemistry and Technology of Fuels and Oils, 61(2), 365–371. https://doi.org/10.1007/s10553-025-01876-1
Luc, M., Black, S. K., Myers, M. D., & Czernik, S. (2009). Study of the Neutralization and Stabilization of a Mixed Hardwood Bio-Oil. Energy Fuels, 23(5), 2695–2699. https://doi.org/10.1021/ef8009266
Khamhuatoey, S., Kaewluan, S., Thawornprasert, J., Ye Min, O., Pongraktham, K., & Somnuk, K. (2023). Upgrading Pyrolysis Bio-Oil through Esterification Process and Assessing the Performance and Emissions of Diesel–Biodiesel–Esterified Pyrolysis Bio-Oil Blends in Direct Injection Diesel Engines. ACS Omega, 8(47), 44586–44600. https://doi.org/10.1021/acsomega.3c05007
Baser, B., Hansen, B. B., Morten Nedergaard, P., Anker Degn, J., Schulzke, T., & Jensen, P. A. (2026). Upgrading Wood and Waste Fast Pyrolysis Oils by Esterification. Energy Fuels, 40(12), 6171–6181. https://doi.org/10.1021/acs.energyfuels.5c06144
EXISTING LITERATURE
1-Hexanol (act as entrainer & alcohol) + Amberlyst-36
>70% TAN reduction and marine-grade flash point achieved (Baser et al., 2026)
Methanol + H₂SO₄ (Without Entrainer)
96.95% acid value reduction (Khamhuatoey et al., 2023)
Methanol / Ethanol + Amberlyst-15 (Without Entrainer)
TAN reduced from 106.1 to 33.1 and 40.6 mgKOH/g, respectively (Ilin et al., 2025)
Without entrainer: reverse hydrolysis dominates, preventing complete esterification.
With entrainer: water content significantly reduced
Ethanol + Amberlyst-15 + Cyclohexane
TAN reduced from 92 to 21 mgKOH/g (Moens et al., 2009)